## Slide 1
Addressing Network Operator Challenges in YANG push Data Mesh Integration
thomas.graf@swisscom.com
18. March 2023

## Slide 2
A single link down result in multiple device topology, control-plane and forwarding-plane events being exposed at different times.
Determine which interfaces and BGP peerings are being used first and then observe state. Observe BGP withdrawals and updates, traffic drop spikes and missing traffic. Generate multiple concerns.
Calculate for each observation a concern score between 0 and 1. The higher, the more probable the changes impacted forwarding.
Unify several concerns for one VPN connectivity service to one alert identifier.
From Network to Alert Event Observe multiple perspectives at different times

## Slide 3: L3 VPN Network Anomaly Detection Verify operational changes automatically
Analytical Perspectives
Monitors the network service and wherever it is congested or not.
BGP updates and withdrawals.
UDP vs. TCP missing traffic.
Interface state changes.
Network Events
VPN orange lost connectivity. VPN blue lost redundancy.
VPN blue lost connectivity.
Key Point
AI/ML requires network intent and network modelled data to deliver dependable results.

## Slide 4: From YANG push to Analytics Aiming for an automated processing pipeline
A network operator aims for:
  An automated data processing pipeline which starts with YANG push, consolidates at Data Mesh and ends at Network Analytics.
  Operational metrics where IETF defines the semantics.
  Analytical metrics where network operators gain actionable insights.
We achieve this by integrating YANG push into Data Mesh to:
  Produce metrics from networks with timestamps when network events were observed.
  Hostname and sequence numbers help us to understand from where metrics were exported and measure its delay and loss.
  Forward metrics unchanged from networks
  Learn semantics from networks and validate messages.
  Control semantic changes end to end.

## Slide 5: Evolving Big Data Architecture Domain oriented, like networks
2nd Generation
3rd Generation
current
  Data lake Big data ecosystem
  Kappa Adds streaming for real-time data
  Proprietary Enterprise Data Warehouse
1st Generation
4th Generation
next-step
  Data Mesh Distributed and organized in domains.
From Principles to Logical Architecture

## Slide 6: Evolving YANG Push Missing puzzle pieces
YANG Push | Today at Network Operators | Today at IETF
Transport Protocol | Many and non-standard | netconf-https-notif and netconf-udp-notif
Encoding | JSON widely adopted. Propriety protobuf in various variants. CBOR not implemented yet. | JSON and XML in RFC8040, CBOR in RFC9254
Subscription | Non-standard, periodical widely adopted. On-change sparse. | RFC8639 and RFC8641
Metadata | Non-standard. Partially among message content. | netconf-yang-notifications-versioning, draft-tgraf-netconf-notif-sequencing, draft-tgraf-yang-push-observation-time, draft-claise-opsawg-collected-data-manifest, draft-claise-netconf-metadata-for-collection
Versioning | Neither covered in subscription nor in publishing. | netmod-yang-module-versioning
YANG module | Non-standard widely adopted. IETF coverage non-existent. | Many RFC's defined

## Slide 7: State of the Union From data mess to data mesh
IETF
Data Industry
Network Vendor/Operator

## Slide 8: YANG datastores enabling Closed Loop Operation Automated data onboarding with bounded context
YANG is a data modelling language which will not only transform how we managed our networks; it will transform also how we manage our services.
News: 17 industry leading colleagues from 4 network operators, 2 network and 3 analytics providers, and 3 universities commit on a project to integrate YANG and CBOR into data mesh. IETF 116 public side meeting on Wednesday March 29th 12:00 – 12:45.
Automated networks can only run with a common data model. A digital twin YANG data store enables a comparison between intent and reality. Schema preservation enables closed loop operation. Closed Loop is like an autopilot on an airplane. We need to understand what the flight envelope is to keep the airplane within. Without, we crash.

## Slide 9
Data Mesh is a big data architecture where different domains can exchange data with a bounded context and SLO's are defined in Data Products. Same principle as in networks.
Semantics are needed to describe the data. A gauge32 is not the same as counter32. Values can increase or decrease. Needs monotonic increasing counter normalization or not.
Versioning is needed to not only understand that the semantic has changed, but also wherever the new semantic is backward compatible or not. Preventing to break the data processing pipeline.
Hostname, sequence numbers and observation timestamping are needed to measure loss and delay for SLO's.
YANG push as defined in RFC8641 is missing hostname, sequence numbers, observation timestamping and versioning. draft-ahuang-netconf-notif-yang, draft-tgraf-netconf-notif-sequencing, draft-tgraf-yang-push-observation-time and draft-tgraf-netconf-yang-notifications-versioning addresses this.
When Big Data and Network becomes one Marrying two messaging protocols

## Slide 11: Define YANG module for Netconf Notifications Closing the semantic gap
module: ietf-notification
structure notification:
+-- eventTime yang:date-and-time
With RFC 5277 the XML schema for NETCONF event notification was defined.
With draft-ahuang-netconf-notif-yang the schema is also defined as a YANG module. Enabling now to define semantics for the entire YANG push message.
<notification xmlns="urn:ietf:params:xml:ns:netconf:notification:1.0">
<eventTime>2023-02-04T16:30:11.22Z</eventTime>
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>1011</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<oper-status>up</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
</notification>

## Slide 12: Extend Streaming Update Notifications with Hostname and Sequencing For push-update and push-change-update
module: ietf-notification-sequencing
augment-structure /inotif:notification:
+-- sysName inet:host
+-- sequenceNumber yang:counter32
When the NETCONF event notification message is forwarded from the YANG push receiver to another system, such as a messaging system or a time series database where the message is stored, the transport context is lost since it is not part of the NETCONF event notification message metadata. Therefore, the downstream system is unable to associate the message to the publishing process (the exporting router), nor able to detect message loss or reordering.
draft-tgraf-netconf-notif-sequencing extends the NETCONF notification defined in RFC5277 with:
  sysName: Describes the hostname following the 'sysName' object definition in RFC1213 from where the message was published from.
  sequenceNumber: Generates a unique sequence number as described in RFC9187 for each published message.
<notification xmlns="urn:ietf:params:xml:ns:netconf:notification:1.0">
<eventTime>2023-02-04T16:30:11.22Z</eventTime>
<sysName xmlns="urn:ietf:params:xml:ns:yang:ietf-notification-sequencing">
example-router
</sysName>
<sequenceNumber xmlns="urn:ietf:params:xml:ns:yang:ietf-notification-sequencing">
187653
</sequenceNumber>
<push-update xmlns="urn:ietf:params:xml:ns:yang:ietf-yang-push">
<id>1011</id>
<datastore-contents>
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>eth0</name>
<oper-status>up</oper-status>
</interface>
</interfaces>
</datastore-contents>
</push-update>
</notification>

## Slide 13: Extend Streaming Update Notifications with Observation Timestamping For push-update and push-change-update
module: ietf-yang-push-netobs-timestamping
augment /yp:push-update:
+--ro observation-time? yang:date-and-time
augment /yp:push-change-update:
+--ro state-changed-observation-time? yang:date-and-time
To correlate network data among different Network Telemetry planes as described in Section 3.1 of RFC9232 or among different YANG push subscription types defined in Section 3.1 of RFC8641, network observation timestamping is needed to understand the timely relationship among these different planes and YANG push subscription types.
draft-tgraf-yang-push-observation-time extends the YANG push streaming update notification defined in RFC8641 with:
  observation-time: Describes the measurement observation time for the "push-update" notification in a "periodical" subscription.
  state-changed-observation-time: Describes in the "push-change-update" notification in an "on-change" subscription the time when the network state change was observed after the subscription was initially established. In case of an "on-change sync on start" subscription it describes the time when the network state change was observed before the subscription was established.
{
"ietf-notification:notification": {
"eventTime": "2023-02-04T16:30:11.22Z",
"sysName": "example-router",
"sequenceNumber": 187653,
"ietf-yang-push:push-update": {
"id": 1011,
"observation-time": "2023-02-04T16:30:09.44Z",
"datastore-xpath-filter": "ietf-interfaces:interfaces",
"datastore-contents": {
"ietf-interfaces:interface": {
"name": {
"eth0": {
"oper-status": "up"
}
}
}
}
}
}
}

## Slide 14: Extend Datastore Selection and Subscription State Change Notifications with revision and revision-label
module: ietf-yang-push-revision
augment /sn:establish-subscription/sn:input/sn:target:
+--rw revision? rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:modify-subscription/sn:input/sn:target:
+--rw revision? rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:subscription-started/sn:target:
+--ro revision rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:subscription-modified/sn:target:
+--ro revision rev:revision-date-or-label
+-- revision-label? ysver:version
augment /sn:subscriptions/sn:subscription/sn:target:
+--ro revision rev:revision-date-or-label
+--rw revision-label? ysver:version
Network operators need to control semantics in its data processing pipeline. That includes YANG push.
This is today only possible during YANG push subscription but not when nodes are being upgraded or messages are being published for configured subscription.
draft-tgraf-netconf-yang-notifications-versioning extends the YANG push subscription and publishing mechanism defined in RFC8641:
  By adding the ability to subscribe to a specific revision or latest-compatible-semversion.
  By extending the YANG push Subscription State Change Notifications Message so that the YANG push receiver learns beside the xpath and the sub-tree filter also the revision and revision-label.
{
"ietf-restconf:notification" : {
"eventTime": "2023-01-03T10:00:00Z",
"ietf-subscribed-notifications:subscription-modified": {
"id": 101,
"revision": "2014-05-08",
"revision-label": "1.0.0",
"stream-xpath-filter": "/ietf-interfaces:interfaces",
"stream": {
"ietf-netconf-subscribed-notifications" : "NETCONF"
}
}
}
}

## Slide 15: From YANG push to Analytics Next steps
Do you realize the gaps and how it could be resolved?
  By defining a YANG module for NETCONF notification and adding hostname, sequence number, observation time, revision and revision-label into YANG push-update and Subscription State Change notification messages an automated data processing pipeline which starts with YANG push, consolidates at Data Mesh and ends at Network Analytics would become at reach.
Collaborate with different network operators, network and analytic vendors and universities on bringing YANG semantics into Apache Kafka.
-> What are your thoughts and comments?
-> Interested to learn more? Join the IETF 116 public side meeting on Wednesday March29th 12:00-12:45 or look at the project page: https://github.com/graf3net/draft-daisy-kafka-yang-integration/blob/main/draft-daisy-kafka-yang-integration-03.md
thomas.graf@swisscom.com
18. March 2023